## Slide 1: UNIT-II Sheet Resistance (Rs)
IC resistors have a specified thickness – not under the control of the circuit designer
Eliminate t by absorbing it into a new parameter: the sheet resistance (Rs)

  
W 
 t W 
Wt
sq 
R  L     L   R  L 
“Number of “quares”
6/3/2015
112

## Slide 2: BASIC ELECTRICAL PROPERTIES
6/3/2015
Topics
Basic electrical properties of MOS and BiCMOS circuits:
Ids-Vds relationships
MOS transistor threshold voltage, gm, gds
figure of merit wo
pass transistor
NMOS inverter
Various pull-ups
CMOS inverter analysis and design
BiCMOS inverters

## Slide 3: MOSFET I-V Characteristics I-V Plots, Channel Length Modulation
– Saturation equation yields curves independent of
VDS. Not sure! So
Quadratic Relationship
0
0.5
1
1.5
0
we consider the effect of channel 1 length modulation.
2
3
4
5
6
x 10
-4
VDS(V)
ID (A)
VGS= 1.5 V
VGS= 1.0 V
2 2.5
VGS= 2.5 V
Resistive Saturation
VGS= 2.0 V
VDS = VGS - VT
130

## Slide 4: MOSFET I-V Characteristics Channel Length Modulation
Channel Length
Modulation
With pinch-off the channel at the point y such that Vc(y)=VGS - VT0, The effective channel length is equal to L’ = L – ΔL
ΔL is the length of channel segment over which QI=0.
Place L’ in the
ID(SAT) equation:
)2
2
I D ( SAT )

L V GS V T 0
 n Cox W (
Source
n+
Drain
n+
Substrate (p-Si)
(p+)
(p+)
Oxide
0
y
L’ ΔL L
Channel
Pinch-off point (QI=0)
Depletion region
VB=0
VS=0
VGS>VT0
VDS>VDSAT

## Slide 5: MOSFET I-V Characteristics Channel Length Modulation
– ΔL increases with an increase in VDS.
We can use
–
λ: channel length modulation coefficient
– ID(SAT) can be rewritten as
– The above form produces a discontinuity of current at VDS=VGS- VT0. We can include the term in ID(lin) with little error since λ is typically less than 0.1. We will usually ignore λ in manual calculations.
L
ΔL
L
L
L
DS
DS
 1 1  V 
1 
 1 1  1 1
L 1  V
 1 1
L L  ΔL
1  1
L' L  ΔL
2 L
DS
GS T 0
I D ( SAT )
V )2 (1  V )
 n Cox W (V

## Slide 6: MOSFET I-V Characteristics Substrate Bias Effect
So far, VSB=0 and thus VT0 used in the equations.
Clearly not always true – must consider body effect
– Two MOSFETs in series:
–
–
– V“B(M1) = VD“(M2) ≠ 0. Thus, VT0 in the M1 equation is replaced
by VT = VT(VSB) as developed in the threshold voltage section.
D
S
D
M1 G
M2 G
VSB
S

## Slide 7: MOSFET I-V Characteristics Substrate Bias Effect (Cont.)
The general form of ID can be written as
ID = f (VGS,VDS,VSB)
which due to the body effect term is non- linear and more difficult to handle in manual calculations

## Slide 8: MOSFET I-V Characteristics Summary of Analytical Equations
– The voltage directions and relationships for the three modes of pMOS are in contrast to those of nMOS.
G
D
B
S
VSB VDS
VGS
ID
G
S
VDS
VSB B
V
GS
ID
D
nMOS |  | 
Mode | ID | Voltage Range
Cut-off | 0 | VGS<VT
Linear | (µnCox/2)(W/L)[2(VGS- VT)VDS-VDS2] | VGSVT，VDS< VGS -VT
Saturatio n | (µnCox/2)(W/L)(VGS- VT)2(1+hVDS) | VGS  VT，VDS  VGS -VT
pMOS |  | 
Cut-off | 0 | VGS>VT
Linear | (µnCox/2)(W/L)[2(VGS- VT)VDS-VDS2] | VGS  VT，VDS> VGS -VT
Saturatio n | (µnCox/2)(W/L)(VGS- V )2(1+hV ) | VGS  VT，VDS135 V -V

## Slide 9: Pass-Transistor Logic Circuits (1)
A simple approach for implementing logic functions utilizes series and parallel combinations of switches that are controlled by input variables to connect the input and output nodes.
Each of the switches can be implemented either by a single NMOS transistor or by a pair of CMOS transistors connected in CMOS transmission gate
configuration.
Y=AC
136

## Slide 10: Pass-Transistor Logic Circuits (2)
6/3/2015
137
An essential requirement in the design of pass-transistor logic is ensuring that every circuit node has at all times a low-resistance path to VDD or to ground.
A basic design requirement of PTL circuits is that every node have, at all times, a low resistance
path to either ground or VDD. Such a path does not exist in (a) when B is low and S1 is open. It is provided in
(b) through switch S2.

## Slide 11: Pass-Transistor Logic Circuits (3)
The problem can be easily solved by establishing for node Y a low- resistance path that is activated when B goes low.
A basic design requirement of PTL circuits is that every node have, at all times, a low resistance
path to either ground or VDD. Such a path does not exist in (a) when B is low and S1 is open. It is provided in
(b) through switch S2.

## Slide 12: MOSFET Ids-Vds

## Slide 13: I-V Characteristics
In Linear region, Ids depends on
  How much charge is in the channel?
  How fast is the charge moving?

## Slide 14: Channel Charge
MOS structure looks like parallel plate capacitor while operating in inversion
– Gate – oxide – channel
Qchannel =
n+ n+
Vgd
gate
+
+
source Vgs
-
+
drain
Vds
p-type body
channel
-
-
Vg
V
s
V
d
Cg
n+
n+
p-type body
W
L
tox
SiO2 gate oxide
ox
(good insulator,  = 3.9)
polysilicon gate

## Slide 15: Channel Charge
n+ n+
Vgd
MOS structure looks like parallel plate capacitor while operating in inversion
– Gate – oxide – channel
Qchannel = CV
C =
gate
+
+
source Vgs
-
+
drain
Vds
p-type body
channel
-
-
Vg
V
s
V
d
Cg
n+
n+
p-type body
W
L
tox
SiO2 gate oxide
ox
(good insulator,  = 3.9)
polysilicon gate

## Slide 16: Channel Charge
MOS structure looks like parallel plate capacitor while operating in inversion
– Gate – oxide – channel
Qchannel = CV
C = Cg = eoxWL/tox = CoxWL
V =
n+ n+
Vgd
gate
+
+
source Vgs
-
+
drain
Vds
p-type body
channel
-
-
Vg
V
s
V
d
Cg
n+
n+
p-type body
W
L
tox
SiO2 gate oxide
ox
(good insulator,  = 3.9)
polysilicon gate
Cox = ox / tox

## Slide 17: Channel Charge
MOS structure looks like parallel plate capacitor while operating in inversion
– Gate – oxide – channel
Qchannel = CV
C = Cg = eoxWL/tox = CoxWL
V = Vgc – Vt = (Vgs – Vds/2) – Vt
n+ n+
Vgd
gate
+
+
source Vgs
-
+
drain
Vds
p-type body
channel
-
-
Vg
V
s
V
d
Cg
n+
n+
p-type body
W
L
tox
SiO2 gate oxide
ox
(good insulator,  = 3.9)
polysilicon gate
Cox = ox / tox

## Slide 18: Carrier velocity
Charge is carried by e-
Carrier velocity v proportional to lateral E-field between source and drain

## Slide 19: Carrier velocity
150
Charge is carried by e-
Carrier velocity v proportional to lateral E-field between source and drain
v = mE m called mobility
E =energy

## Slide 20: Carrier velocity
Charge is carried by e-
Carrier velocity v proportional to lateral E-field between source and drain
m called mobility
v = mE
E = Vds/L
Time for carrier to cross channel:
– t =

## Slide 21: Carrier velocity
Charge is carried by e-
Carrier velocity v proportional to lateral E-field between source and drain
m called mobility
v = mE
E = Vds/L
Time for carrier to cross channel:
– t = L / v

## Slide 22: nMOS Linear I-V
Now we know
  How much charge Qchannel is in the channel
  How much time t each carrier takes to cross
Ids


## Slide 23: nMOS Linear I-V
Now we know
  How much charge Qchannel is in the channel
  How much time t each carrier takes to cross
ds
I
t
 Qchannel


## Slide 24: nMOS Linear I-V
Now we know
– How much charge Qchannel is in the channel
ox
ds
gs
t
ds
gs t
ds
– HoQw much time t each carrier takes to cross
I
 channel
t
 C
V  Vds
W V
V
L 
2 
V
  V V Vds

2 


ox
W L
 = C

## Slide 25: nMOS Saturation I-V
If Vgd < Vt, channel pinches off near drain
– When Vds > Vdsat = Vgs – Vt
Now drain voltage no longer increases current
Ids


## Slide 26: nMOS Saturation I-V
If Vgd < Vt, channel pinches off near drain
– When Vds > Vdsat = Vgs – Vt
Now drain voltage no longer increases current
ds
gs
t
dsat
V Vdsat
I   V
V

2 

## Slide 27: nMOS Saturation I-V
If Vgd < Vt, channel pinches off near drain
– When Vds > Vdsat = Vgs – Vt
Now drain voltage no longer increases current

2
2
ds
gs t
dsat
gs t
V Vdsat
I   V
V

2 
  V V

## Slide 28: nMOS I-V Summary
Shockley 1st order transistor models

2
cutoff
linear
0
2
saturation
ds
gs
t
ds
ds
dsat
gs
Vgs  Vt



V Vds
V  V
I   V
V


2 
V Vt 
Vds  Vdsat

 


## Slide 29: Example
Example: a 0.6 mm process from AMI semiconductor
– tox = 100 Å
– m = 350 cm2/V*s
– Vt = 0.7 V
Plot Ids vs. Vds
– Vgs = 0, 1, 2, 3, 4, 5
– Use W/L = 4/2 l
 
2
ox
W L
 A /V
14
 W
W  3.9  8.8510
L
 
  C
 350
 120

  L 
100 108

  
0
1
2
3
4
5
0
0.5
1
1.5
2
2.5
Vds
Ids (mA)
Vgs = 5
gs
V = 4
Vgs = 3
Vgs = 2
Vgs = 1
6/3/2015
160

## Slide 30
Vdd
Vo
Vin
R
Pull-Up
Pull Down
Basic Inverter: Transistor with source connected to ground and a load resistor connected from the drain to the positive Supply rail
Output is taken from the drain and control input connected between gate and ground
Resistors are not easily formed in silicon
- they occupy too much area
Transistors can be used as the pull-up device
Vss

## Slide 31
Vdd
Vss
Vo
Vin
D
S
D
S
Pull-Up is always on – Vgs = 0; depletion
Pull-Down turns on when Vin > Vt
NMOS Depletion Mode Transistor Pull - Up
Vt
V0
Vdd
Vi
With no current drawn from outputs, Ids
for both transistors is equal
Non-zero output

## Slide 32
Vgs=0.6 VDD
Vgs=0.4 VDD Vgs=0.2VDD
Vgs=0.8VDD
Vgs=VDD
Ids
Vds
VDD
V
o
VDD
VDD
Vin
VDD –Vds
Ids
V
ds
Vgs=0
Vgs=-0.2 VDD Vgs=-0.4 VDD Vgs=-0.6VDD
Ids
Vgs=0.2VDD

## Slide 33: Decreasing Zpu/Zpd
Vo
V
DD
VDD
Vin
Vinv
Increasing
Zpu/Zpd
Point where Vo = Vin is called Vinv
Transfer Characteristics and Vinv can be shifted by altering ratio
of pull-up to Pull down impedances

## Slide 34: NMOS Depletion Mode Inverter Characteristics
Dissipation is high since rail to rail current flows when Vin = Logical 1
Switching of Output from 1 to 0 begins when Vin exceeds Vt of pull down device
When switching the output from 1 to 0, the pull up device is non-saturated initially and this presents a lower resistance through which to charge capacitors (Vds < Vgs – Vt)

## Slide 35
Vss
Vo
Vin
D
S
D
S
NMOS Enhancement Mode Transistor Pull - Up
Vdd
Vgg
Vt (pull down)
V0
Vdd
Vt (pull up)
Non zero output
Vin
Dissipation is high since current flows when Vin = 1
Vout can never reach Vdd (effect of channel)
Vgg can be derived from a switching source (i.e. one phase of a clock, so that dissipation can be significantly reduced
If Vgg is higher than Vdd, and extra supply rail is required

## Slide 36: Cascading NMOS Inverters
When cascading logic devices care must be taken to preserve integrity of logic levels
i.e. design circuit so that Vin = Vout = Vinv
Determine pull – up to pull-down ratio for driven inverter
180

## Slide 37
Assume equal margins around inverter; Vinv = 0.5 Vdd
Assume both transistors in saturation, therefore: Ids = K (W/L) (Vgs – Vt)2/2 Depletion mode transistor has gate connected to source, i.e. Vgs = 0
Ids = K (Wpu/Lpu) (-Vtd)2/2
Enhancement mode device Vgs = Vinv, therefore Ids = K (Wpd/Lpd) (Vinv – Vt)2/2
Assume currents are equal through both channels (no current drawn by load)
(Wpd/Lpd) (Vinv – Vt)2 = (Wpu/Lpu) (-Vtd)2 Convention Z = L/W
Vinv = Vt – Vtd / (Zpu/Zpd)1/2
Substitute in typical values Vt = 0.2 Vdd ; Vtd = -0.6 Vdd ; Vinv = 0.5 Vdd
This gives Zpu / Zpd = 4:1 for an nmos inverter directly driven by another inverter

## Slide 38: Pull-Up to Pull-Down Ratio for an nMOS inverter driven through 1 or more pass transistors
Vdd
Vdd
A
B
C
Inverter 1
Inverter 2
Vin1
Vout2
It is often the case that two inverters are connected via a series of switches (Pass Transistors) We are concerned that connection of transistors in series will degrade the logic levels into Inverter 2. The driven inverter can be designed to deal with this. (Zpu/Zpd >= 8/1)

## Slide 39
Complimentary Transistor Pull – Up (CMOS)
Vdd
Vss
Vo
Vin
Vout
Vin
Vdd
Vss
Vtn
Vtp
Logic 0
Logic 1
P on
N off
Both On
N on
P off

## Slide 40
Vout
Vin
Vdd
Vss
Vtn
Vtp
P on N off
Both On
N on P off
1
2
3
4
5
1: Logic 0 : p on ; n off
5: Logic 1: p off ; n on
2: Vin > Vtn.
Vdsn large – n in saturation Vdsp small – p in resistive Small current from Vdd to Vss
4: same as 2 except reversed p and n
3: Both transistors are in saturation
Large instantaneous current flows

## Slide 41
CMOS INVERTER CHARACTERISTICS
Current through n-channel pull-down transistor
2
2
in tn
n
n
V V
I 

Current through p-channel pull-up transistor
2
2
p
   Vtp
Vin VDD
I p 

At logic threshold, In = Ip

p
n
tp
in DD
p
in tn
n
p
n
Vin VDD Vtp
Vin Vtn
Vtn  VDD  Vtp
 


  Vin  VDD  Vtp
Vin  Vtn
 V  V  V 
V  V  
 
 
   
n
 p
  p 
 n 




Vin 1 
2
2

2

2
2
2
in
n


n
 p
VDD  Vtp  Vtn
V 
1 
If n = p
p
and Vtp = –Vtn
2
VDD
Vin 
 pWp  nWn
Lp Ln
Mobilities are unequal : µn = 2.5 µp
Z = L/W
pu pd
Z /Z = 2.5:1 for a symmetrical CMOS inverter

## Slide 42: CMOS Inverter Characteristics
No current flow for either logical 1 or logical 0 inputs
Full logical 1 and 0 levels are presented at the output
For devices of similar dimensions the p –
channel is slower than the n – channel device

## Slide 43: CMOS Inverter VTC
1
0.5
0
2
1.5
2.5
0
0.5
1
Vin (V)
Vout
(V)
NMOS off PMOS res
NMOS sat
PMOS res
NMOS sat
PMOS sat
NMOS res
PMOS sat
1.5 2
NMOS res P2M.5OS off

## Slide 44: Cutoff
Linear
Saturation
pMOS
Vin -VDD= VGS> VT
Vin -VDD=VGS< VT
Vin -Vout=VGD< VT
Vin -VDD=VGS> VT
Vin -Vout=VGD>VT
nMOS
Vin = VGS< VT
Vin =VGS> VT
Vin -Vout =VGD> VT
Vin =VGS> VT
Vin -Vout =VGD< VT
VDD
Vin
Vout
CL
G
S
D
D
G
S
Regions of operations For nMOS and pMOS In CMOS inverter

## Slide 45: Impact of Process Variation
2.5
2
1.5
0 0.5
1
1.5
2
2.5
Vout
(V)
Nominal
Good PMOS Bad NMOS
1Bad PMOS
0.5Good NMOS
0
Vin (V)
Pprocess variations (mostly) cause a shift in the switching
threshold

## Slide 46: Cmos Inverter
190
Look at why our NMOS and PMOS inverters might not be the best inverter designs
Introduce the CMOS inverter
Analyze how the CMOS inverter works

## Slide 47: NMOS Inverter
When VIN change
cutoff. ID goes to 0.
5 V.
D
D
uI p=”5/tRo
+
V
DS
_
R
5 V
V
OUT
VIN
5 V
0 V
D
ID = 0
+
VDS
_
5 V
V
OUT
VIN
0 V
5 V
When V is logic 1, V
IN OUT
s to logic 0, itsransistor gets
logic 0.
Constant nonzero current R
‘esistor voltagfleowgs othreousghtotraznseisrtoor.. VOUT “pulled
Power is used even though no new computation is being performed.

## Slide 48: PMOS Inverter
OUT
ID = -5/R
down”VtDoS 0V V.
+
R
5 V
When VIN is logic 0, VOUT is logic 1.
Constant nonzero current flows through transistor.
Power is used even though no new computation is being performed.
0 V
When V5INV changes to logic 1, transistor gets5 V
VOUT
ID = 0
- VDS
+
R
0 V
cutoff. ID goes to 0.
V•IN ‘esisto-r voltage goes to zero. VOUVITN “pulled
5 V

## Slide 49: Analysis of CMOS Inverter
circuits.
Remember, now we have two transistors so
we write two I-V relationships and have twice
D
DD
We can foVllow(Lotghice1) same procedure to solve for
D
currents aSnd voltages in the CMOS inverter as we did for the single NMOS and PMOS
VOUT
VIN
the number of variables.
We can roSughly analyze the CMOS inverter
NMOS isg“rpaulpl-dhowicnadlelvyic.e”
PMOS is “pull-up device”
Each shuts off when not pulling

## Slide 50: CMOS Analysis
ID(n)
NMOS I-V curve
PMOS I-V curve (written in terms of NMOS variables)
VIN = VGS(n) =
0.9 V
As VIN goes up, VGS(n) gets bigger
and VGS(p) gets less negative.
VDS(n)
VDD

## Slide 51: CMOS Analysis
ID(n)
NMOS I-V curve
PMOS I-V curve (written in terms of NMOS variables)
VIN = VGS(n) =
4.1 V
As VIN goes up, VGS(n) gets bigger
and VGS(p) gets less negative.
VDS(n)
VDD

## Slide 52: Beta Ratio
If bp / bn  1, switching point will move from VDD/2
Vout
0
Vin
VDD
VDD
2
1
0.5
n


p  10
n


p  0.1

## Slide 53: VLSI CIRCUIT DESIGN PROCESSES
Topics
VLSI design flow
MOS layers
Stick diagrams
Design Rules and Layout
2 um CMOS design rules for wires
Contacts and Transistors
Layout diagrams for NMOS and
CMOS inverters and gates, Scaling of MOS circuits

## Slide 54: VLSI Design of approach of IC
26/038/2015

## Slide 55: Layer Types
209
p-substrate
n-well
n+
p+
Gate oxide (thin oxide)
Gate (polycilicon)
Field Oxide
  Insulated glass
  Provide electrical isolation

## Slide 56
Stick diagram
Encodings for a simple single metal nMOS process
BROWN
COLOR | STICK ENCODING MONOCROME | LAYERS | MASK LAYOUT ENCODING MONOCROME | CIF | LAYER
 |  | n- |  |  | 
GREEN |  | diffusion n+active |  | N D | 
RED |  | Thniox Polysilicon |  | NP | 
BLUE |  | Metal 1 |  | N M | 
BLACK |  | Contact cut |  | N | 
 |  |  |  | C | 
GRAY nMOS ONLY | NOT APPLICABLE | Overglass Implant |  | N G NI | 
YELLO nWMOS ONLY |  | Buried |  | NB | 
 |  | contact |  |  | 
219

## Slide 57: Stick Diagrams
Metal
poly ndiff
pdiff
Can also draw in shades of gray/line style.
Buried Contact
Contact Cut

## Slide 58: Stick Diagrams
VLSI design aims to translate circuit concepts onto silicon.
Stick diagrams are a means of capturing topography and layer information using simple diagrams.
Stick diagrams convey layer information through colour codes (or monochrome encoding).
Acts as an interface between symbolic circuit and the actual layout.

## Slide 59: Stick Diagrams
Does show all components/vias.
It shows relative placement of components.
Goes one step closer to the layout
Helps plan the layout and routing

## Slide 60: Stick Diagrams
Does not show
  Exact placement of components
  Transistor sizes
  Wire lengths, wire widths, tub boundaries.
  Any other low level details such as parasitics..

## Slide 61: Stick Diagrams – Some rules
Rule 1.
When two or more ‘sticks’ of the same type cross or touch each other that represents electrical contact.
Stick Diagrams

## Slide 62: Stick Diagrams – Some rules
Rule 2.
When two or more ‘sticks’ of different type cross or touch each other there is no electrical contact.
(If electrical contact is needed we have to show the connection explicitly).
Stick Diagrams

## Slide 63: Stick Diagrams – Some rules
Rule 3.
When a poly crosses diffusion it represents a transistor.
Note: If a contact is shown then it is not a transistor.
Stick Diagrams

## Slide 64: Stick Diagrams – Some rules
Rule 4.
In CMOS a demarcation line is drawn to avoid touching of p-diff with n-diff. All pMOS must lie on one side of the line and all nMOS will have to be on the other side.
Stick Diagrams

## Slide 66: NMOS INVERTER
5 V
Dep
Vout
Enh
0V
0 V
Vin
5 v
220

## Slide 67: NMOS-NAND

## Slide 68: NMOS-NOR

## Slide 69: NMOS EX-OR

## Slide 70: NMOS EX-NOR

## Slide 71: PMOS-INVERTER

## Slide 72: PMOS NAND

## Slide 73: PMOS-NOR

## Slide 74: Sticks design CMOS NAND:
Start with NAND gate:

## Slide 75: NAND sticks
VDD
a
out
b
VSS

## Slide 76: Stick Diagram - Example
OUT
B
NOR Gate
A
230

## Slide 77: Stick Diagram - Example
Power
Ground
C
B
Out
A

## Slide 78: 2 I/P OR GATE

## Slide 79: 2 I/P AND

## Slide 81: Y=(AB+CD)’

## Slide 82: Y=(AB+CD)’ “TICK

## Slide 84: Design Rules
Design rules are a set of geometrical specifications that dictate the design of the layout masks
A design rule set provides numerical values
  For minimum dimensions
  For minimum line spacings
Design rules must be followed to insure functional structures on the fabricated chip
Design rules change with technological advances (www.mosis.org)

## Slide 85: Design Rules
Minimum length or width of a feature on a layer is 2
Why?
To allow for shape contraction
Minimum separation of features on a layer is 2
Why?
To ensure adequate continuity of the intervening materials.

## Slide 86: Design Rules
Minimum width of PolySi and diffusion line 2
Minimum width of Metal line 3 as metal lines run over a more uneven surface than other conducting layers to ensure their continuity

Metal
Diffusion
Polysilicon



## Slide 87: Design Rules
PolySi – PolySi space 2 Metal - Metal space 2
Diffusion – Diffusion 3 To avoid the possibility of their associated regions overlapping and conducting current

Metal
Diffusion
Polysilicon


250

## Slide 88: Design Rules
Diffusion – PolySi  To prevent the lines overlapping to form unwanted capacitor
Metal lines can pass over both diffusion and polySi without electrical effect. Where no separation is specified, metal lines can overlap or cross

Metal
Diffusion
Polysilicon

## Slide 89: Metal Vs PolySi/Diffusion
Metal lines can pass over both diffusion and polySi without electrical effect
It is recommended practice to leave  between a metal edge and a polySi or diffusion line to which it is not electrically connected

Metal
Polysilicon

## Slide 90: Review:
poly-poly spacing 2
diff-diff spacing 3
(depletion regions tend to spread outward)
metal-metal spacing 2
diff-poly spacing 

## Slide 91: Note
Two Features on different mask layers can be misaligned by a maximum of 2l on the wafer.
If the overlap of these two different mask layers can be catastrophic to the design, they must be separated by at least 2l
If the overlap is just undesirable, they must be separated by at least l

## Slide 92: When a transistor is formed?
Gate is formed where polySi crosses diffusion with
thin oxide between these layers.
Design rules
min. line width of polySi and diffusion 2
drain and source have min. length and width of 2
And

## Slide 93: PolySi extends in the gate region…
The polySi of the gate extends 2 beyond the gate area on
to the field oxide to prevent the drain and source from shorting.
no overlap
overlap
diffusion short
Diffusion Problems

## Slide 94: Depletion Transistor
We need depletion implant
An implant surrounding the Transistor by 2
Ensures that no part of the transistor remains in the enhancement mode
A separation of 2 from the gate of an enhancement transistor avoids affecting the device.
2

## Slide 95: Depletion Transistor
Implants are separated by 2 to prevent them from merging
2

## Slide 96: Butting Contact
The gate and source of a depletion device can be connected by a method known as butting contact. Here metal makes contact to both the diffusion forming the source of the depletion transistor and to the polySi forming this device’s gate.
Advantage:
No buried contact mask required and avoids associated processing.

## Slide 97: Butting Contact
n+
n+
Gate Oxide
PolySi
Problem: Metal descending the hole has a tendency to fracture at the polySi corner, causing an open circuit.
Metal
Insulating
Oxide
260

## Slide 98: Buried Contact
It is a preferred method. The buried contact window defines the area where oxide is to be removed so that polySi connects directly to diffusion.
Contact Area must be a min. of 2*2 to ensure adequate contact area.
2
Contact Area
2
6/3/2015
261

## Slide 99: Buried Contact
The buried contact window surrounds this contact by  in all
directions to avoid any part of this area forming a transistor.
Separated from its related transistor gate by  to prevent gate area from being reduced.


## Slide 100: Buried Contact
 2  |  | 
 | 2 | 
Here gate length is depend upon the alignment of the buried contact mask relative to the polySi and therefore vary by .
PolySi
Channel length 
Buried contact Diffusion

## Slide 101: Contact Cut
Metal connects to polySi/diffusion by contact cut. Contact area: 22
Metal and polySi or diffusion must overlap this contact area by  so that the two desired conductors encompass the contact area despite any mis-alignment between conducting layers and the contact hole
4 |  | 

## Slide 102: Contact Cut
Contact cut – any gate: 2 apart
Why? No contact to any part of the gate.
4
2

## Slide 103: Contact Cut
Contact cut – contact cut: 2 apart Why? To prevent holes from merging.
2

## Slide 104: Rules for CMOS layout
Similar to those for NMOS except No
Depletion implant
Buried contact
Additional rules
  Definition of n-well area
  Threshold implant of two types of transistor
  Definition of source and drains regions for the NMOS and PMOS.

## Slide 105: Rules for CMOS layout
To ensure the separation of the PMOS and NMOS devices, n-well supporting PMOS is 6 away from the active
area of NMOS transistor.
Why?
Avoids overlap of the associated regions
n-well
n+
6

## Slide 106: Rules for CMOS layout
2
2
N-well must completely surround the PMOS device’s active area by 2

## Slide 107: Rules for CMOS layout
2
2
The threshold implant mask covers all n-well and surrounds the n-well by 
270

## Slide 108: Rules for CMOS layout
2
2
The p+ diffusion mask defines the areas to receive a p+ diffusion.
It is coincident with the threshold mask surrounding the PMOS transistor but excludes the n-well region to be connected to the supply.

## Slide 109: Rules for CMOS layout
A p+ diffusion is required to effect the ground connection to the substrate. Thus mask also defines this substrate region. It surrounds the conducting material of this contact by 
4

## Slide 110: Rules for CMOS layout
Total contact area = 24
Neither NMOS nor CMOS usually allow contact cuts to the gate of a transistor, because of the danger of etching away part of the gate