## Slide 1: UNIT IV DATAPATH SUBSYSTEMS
Topics
Sub system design,
Shifters,
Adders,
ALUs,
Multipliers,
Parity generators,
Comparators,
Zero/One detectors,
Counters.

## Slide 2: 1’s & 0’s Detectors
1’s detector: N-input AND gate
0’s detector: NOTs + 1’s detector (N-input NOR)
299
4
A3 A2
A1 A0
A
5
A
A7 A6
allones
0
1
A
A3 A2
A
allzeros
allones
A
1
A7 A6
A5 A4
A3 A2
A0
6/3/2015

## Slide 3: Comparators
300
0’s detector:
1’s detector:
A = 00…000 A = 11…111
Equality comparator: A = B
Magnitude comparator: A < B

## Slide 4: Equality Comparator
A = B
A[3]
B[2]
A[2]
B[1]
A[1]
B[0]
A[0]
Check if each bit is equal (XNOR, aka equality gate)
1’s detect on bitwise equality
B[3]
301

## Slide 5: Magnitude Comparator
Compute B – A and look at sign
B – A = B + ~A + 1
For unsigned numbers, carry out is sign bit
B3
A3 B2
A2 B1
A1 B0
A0
A = B
Z
A  B
C
N
A  B
302

## Slide 6: Signed vs. Unsigned
For signed numbers, comparison is harder
  C: carry out
  Z: zero (all bits of B – A are 0)
  N: negative (MSB of result)
  V: overflow (inputs had different signs, output sign
 B)
  S: N xor V (sign of result)
–
303

## Slide 7: Shifters
Logical Shift:
– “hifts number left or right and fills with 0’s
1 1011 L
SL1 = 0110
1011 LSR 1 = 010
Arithmetic Shift:
– Shifts number left
or right
. Rt shift sign
extends
1011 ASL1 = 0110
1011 ASR1 = 1101
Rotate:
– Shifts number left
or righ
t and fills with lo
st bits
1011 ROR1 = 1101
1011 ROL1 = 0111
304

## Slide 8: Adders
305
Single-bit Addition
Carry-Ripple Adder
Carry-Skip Adder
Carry-Look ahead Adder
Carry-Select Adder
Carry-Increment Adder
Tree Adder

## Slide 9: Barrel Shifter
Barrel shifters perform right rotations using wrap-around wires.
Left rotations are right rotations by N – k = k + 1 bits.
Shifts are rotations with the end bits masked off.
306

## Slide 10: Single-Bit Addition
Half Adder
Full Adder
0
0
0
1
0
1
A | B | Cout | S
0 | 0 |  | 
0 | 1 |  | 
1 | 0 |  | 
1 | 1 |  | 
1
0
0
0
0
1
0
1
1
0
0
1
1
0
1
0
A | B | C | Cout | S
0 | 0 | 0 |  | 
0 | 0 | 1 |  | 
0 | 1 | 0 |  | 
0 | 1 | 1 |  | 
1 | 0 | 0 |  | 
1 | 0 | 1 |  | 
1 | 1 | 0 |  | 
1 | 1 | 1 |  | 
1
1
A B
S
C
out
A B
C
S
Cout
out
S  A  B
C  A B
S  A  B  C
Cout  MAJ ( A, B,C)
307

## Slide 11: PGK
ms of
B
 B
For a full adder, define what happens to carries
  (in ter A and B)
Generate: Cout = 1 independent of C
  G = A •
Propagate: Cout = C
  P = A
Kill: Cout = 0 independent of C
• K = ~A • ~B
308

## Slide 12: Full Adder Design I
Cout
Brute force implementation from eqns
S  A  B  C
 MAJ ( A, B,C)
A B C
S
C
out
MAJ
A B C
A
B
B
C
S
C
B
B
B
C
C
A
A
A
B
A
B
C
B
A
C
B
A
A
B
C
C
out
C
A
B A
B
309

## Slide 13: Full Adder Design II
•
S
S
Cout
A
addeB r
C
Cout
Factor S in terms of Cout
S = ABC + (A + B + C)(~Cout)
Critical pathMINiOsRITuY sually C to Cout in ripple
310

## Slide 14: Layout
Clever layout circumvents usual line of diffusion
  Use wide transistors on critical path
  Eliminate output inverters
311

## Slide 15: Full Adder Design III
A
C
B
B
C
S
C
C
B
S
C
C
Cout
C
C
Cout
Complementary Pass Transistor Logic (CPL)
– Slightly faster, but more areBa
B
B
B
B
B
B
B
A
A
B
A
312

## Slide 16: Full Adder Design IV
Cout _h
C_h A_h A_h B_h B_h
out
C _l
A_l
C_l A_l
B_l B_l
Dual-rail domino
  Very fast, but large and power hungry
  Used in very fast multipliers
S_h
S_l
A_h
B_h
B_h
B_l
A_l
C_h
C_h

C_l
313

## Slide 17: Carry Propagate Adders
N-bit adder called CPA
  Each sum bit depends on all previous carries
  How do we compute all these carries quickly?
+
BN...1
AN...1
S
N...1
C
in
C
out
Cout Cin
11111 carries
1111 A4...1
+0000 B4...1
0000 S4...1
00000
1111
+0000
1111
Cin
314
Cout

## Slide 18: Carry-Ripple Adder
Cin
Cout
Simplest design: cascade full adders
  Critical path goes from Cin to Cout
  Design full adder to have fast carry delay
A4 B4 A3 B3 A2 B2 A1 B1
315
S1
S2
S3
S4
C
1
C
2
C
3

## Slide 19: Inversions
Cout
Cin
Critical path passes through majority gate
  Built from minority + inverter
  Eliminate inverter and use inverting full adder
A4 B4 A3 B3 A2 B2 A1 B1
S1
S2
S3
S4
C1
C2
C3
316

## Slide 20: Generate / Propagate
Equations often factored into G and P
Generate and propagate for groups spanning i:j
Base case
Pi:k Gk 1: j
Pk 1: j
Gi: j  Gi:k Pi: j  Pi:k
i:i
i:i
G 
Gi  Ai Bi
P 
Pi  Ai  Bi
G0:0 P0:0
G0  Cin


P0  0
Sum:
Si 
Pi  Gi1:0
317

## Slide 21: PG Logic
S1
B1
G1 P1
G0:0
S2
B2 A1
G2 P2
G1:0
S3
B3 A2
G3 P3
G2:0
S4
B4 A3
G4 P4
G3:0
A4
Cin
G0 P0
1: Bitwise PG logic
2: Group PG logic
3: Sum logic
C0
C1
C2
C3
Cout
C4

## Slide 22: Carry-Ripple Revisited
Gi:0  Gi Gi1:0
Pi
S1
B1
G1 P1
G0:0
S2
B2 A1
G2 P2
G1:0
S3
B3 A2
G3 P3
G2:0
S4
G4 P4
G3:0
A4 B4 A3
Cin
G0 P0
C0
C1
C2
C3
Cout
C4

## Slide 23: Carry-Skip Adder
Carry-ripple is slow through all N stages
Carry-skip allows carry to skip over groups of n bits
Cin
+
S4:1
B4:1
+
S12:9
– DeciAs16i:13oBn16:13based oAn12:9nB1-2:9bit propaA8g:5 aB8t:5 e signal A4:1 P16:13 P12:9 P8:5 P4:1
C
out
C8 1 C4 1
0 + 0
S8:5
C12
1 1
0 + 0
S16:13
320

## Slide 24: Carry-Lookahead Adder
Carry-lookahead adder computes Gi:0 for many bits in parallel.
Uses higher-valency cells with more than two inputs.
Cin
+
S4:1
G4:1 P4:1
A4:1
B4:1
+
S8:5
G8:5 P8:5
A8:5 B8:5
+
S12:9
G12:9 P12:9
A12:9 B12:9
+
S16:13
G16:13 P16:13
A16:13 B16:13
321
C4
C8
C12
Cout

## Slide 25: Carry-Select Adder
Trick for critical paths dependent on late input X
  Precompute two possible outputs for X = 0, 1
  Select proper output when X arrives
in
sB4:u1
S4:1
4
C
0
1
S8:5
C8
0
1
S12:9
+ + + +
0
1
Carry-seAl1e6:13 cB1t6:13 adder pA12:r9 eB12c:9 omputAe8:5 sB8n:5 -bAi4t:1 ms
S16:13
Cout
– For both+ po0 ssible car+rie0s into n-b+it g0roup
322
C12 C
1 1 1

## Slide 26: Carry Save Addition
A full adder sums 3 inputs and produces 2 outputs
– Carry output has twice weight of sum output
N full adders in parallel are called carry save adder
– Produce N sums and N carry outs
327
C4 S4
X4 Y4 Z4 X3 Y3 Z3 X2 Y2 Z2 X1 Y1 Z1
C1 S1
C3 S3 C2 S2
XN...1 YN...1 ZN...1
SN...1
CN...1
n-bit CSA
6/3/2015

## Slide 27: CSA Application
4-bit CSA
5-bit CSA
0001 0111 1101 0010
1011
0101_
01010_
00011
Use k-2 stages of CSAs
– Keep result in carry-save redundant form
Final CPA computes actu0a00l1 rXesult
0111 Y
+1101 Z
1011 S
0101_ C
0101_ X
1011 Y
+0010 Z S C
00011
01010_
01010_
00011
10111
+
A
+ B S
10111
328

## Slide 28: Multiplication
Example:
1100 : 1210
0101 : 510
1100
0000
1100
0000
00111100 : 6010
multiplicand multiplier
partial products
product
M x N-bit multiplication
  Produce N M-bit partial products
  Sum these to produce M+N-bit product
329

## Slide 29: General Form
330
Multiplicand: Y = (yM-1, yM-2, …, y1, y0)
Multiplier: X = (xN-1, xN-2, …, x1, x0)
Product:
j
i
j
i
y 2
x 2
xi y j 2
M 1
N 1 M 1
i j
  N 1

P 




   
 j0   i0
 
y
5
y
4
y
3
y
2
y
1
 i0 j0
y
0
3 5
3 4
3 3
3 2
3 1
3 0
multiplicand
 |  | x5 | x4 | x3 | x2 | x1 | x0 | multiplier
 |  | x0y5 | x0y4 | x0y3 | x0y2 | x0y1 | x0y0 | 
 |  | x1y5 x1y4 | x1y3 | x1y2 | x1y1 | x1y0 |  | 
 | x2y5 | x2y4 x2y3 | x2y2 | x2y1 | x2y0 |  |  | partial
 | x y x y | x y x y | x y | x y |  |  |  | products
x4y5 | x4y4 x4y3 | x4y2 x4y1 | x4y0 |  |  |  |  | 
x5y5 x5y4 | x5y3 x5y2 | x5y1 x5y0 |  |  |  |  |  | 
p11 p10 p9 | p8 p7 | p6 p5 | p4 | p3 | p2 | p1 | p0 | product

## Slide 30: Dot Diagram
Each dot represents a bit
partial products
multiplier x
331
x0
x15

## Slide 31: Array Multiplier
6/3/2015
332
y0
y1
y2
y3
x0
x1
x2
x3
p0
p1
p2
p3
p4
p6
p7
B
Sin A Cin
Cout Sout
p5
A B
Cin
Cout
Sout
Sin
=
CSA
Array
CPA
critical path
B
A
Sout
Cout
Cin
Cout
Sout
Cin =
B
A

## Slide 32: Rectangular Array
Squash array to fit rectangular floorplan
y3 y2 y1 y0
x0
333
x
1
x
2
x
3
p0
p1
p2
p3
p4
p5
p6
p7

## Slide 33: Booth Encoding
Instead of 3Y, try –Y, then increment next partial product to add 4Y
Sim pro
ilarly, for 2Y, try –2Y + 4Y in next partial
duct
335

## Slide 34: Booth Hardware
Booth encoder generates control lines for each P
– Bo
P
oth selectors choose PP bits
336

## Slide 35: Advanced Multiplication
337
Signed vs. unsigned inputs
Higher radix Booth encoding
Array vs. tree CSA networks

## Slide 36: Array Sub Systems
Topics:
SRAM DRAM ROM
Serial Access Memories
Content Addressable Memory
338

## Slide 37: Semiconductor Memory Types
Semiconductor Memories
Read/Write (R/W) Memory
or Random Access Memory (RAM)
Read-Only Memory (ROM)
Mask (Fuse) ROM
Programmable ROM (PROM) Erasable PROM (EPROM)
Electrically Erasable PROM (EEPROM)
Flash Memory
Ferroelectric RAM (FRAM)
Dynamic RAM (DRAM)
Static RAM (SRAM)
339

## Slide 38: Semiconductor Memory Types (Cont.)
349
Design Issues
» Area Efficiency of Memory Array:  of stored data bits per
unit area
» Memory Access Time: the time required to store and/or retrieve a particular data bit.
» Static and Dynamic Power Consumption
  Requirements
» Easy reading
» Easy Writing
» High density
» Speed, more speed and still more speed

## Slide 39: Memory Architecture
Stores large number of bits
m x n: m words of n bits each
k = Log2(m) address input signals
or m = 2k words
e.g., 4,096 x 8 memory:
» 32,768 bits
» 12 address input signals
» 8 input/output data signals
Memory access
m × n memory
 |  |  |  | … | 
… |  |  |  |  | 
m words
2k × n read and write memory
…
r/w
…
r/w: selects read or write
enable: read or write only when asserted
multiport: multiple accesses to different locations simultanQne-1ouslyQ0
enabl
eA
0
Ak-1
341
n bits per word
memory external view

## Slide 40: Semiconductor Memory Types (Cont.)
342
RAM: the stored data is volatile
  DRAM
» A capacitor to store data, and a transistor to access the capacitor
» Need refresh operation
» Low cost, and high density  it is used for main memory
  SRAM
» Consists of a latch
» Don’t need the refresh operation
» High speed and low power consumption it is mainly used for cache memory and memory in hand-held devices

## Slide 41: RAM: “Random-access” memory
Typically volatile memory
bits are not held without power supply
ssor
during execution
c tha
s stor
t stores
ed bit when
rd/wr indicates read
2k × n read and write memory
A0
Read and written to easily by micropro…ce
r/w
enable
…
Q0
Internal structure more complex than ROMQn-1
Ak-1
External view
4×4 RAM
2×4
i decoder
input data bit when rd/wr indicates write or ouAt0 put
enable
A1
Q3 Q2 Q1 Q0
Memory
cell
I3 I2 I1 I0
rd/wr
343
To every cell
a word consists of several memory cells, each storing 1 Ibnitternal view
each input and output data line connects to each cell in its column
rd/wr connected to every cell
when row is enabled by decoder, each cell has log

## Slide 42: Memory Chip Configuration
Row Dec
Memory Cell Array
Row Address N bits
Complete Address N+M Bits
M
2 Cells
Din
Dout
I/O Control
din
dout
Column Dec.
N
2 Cells
WL
DL
Cell
Control Signals
I/O Interface
s
344
Column Addres M Bits

## Slide 43: Static Random Access Memory (SRAM)
SRAM: ThebitsltionereCd data can be retained inbditelifnienCitely, without any need for a periodic refresh operation.
bit line C
bit line C
load
load
word line word line
Complementary Column arrangement is to achieve a more
reliable SRAM operation
1-bit SRAM cell
VDD
345

## Slide 44: 4T-SRAM(Resistive-Load SRAM Cell )
VDD
bit line C
bit line C
R
R
word line
word line
pass transistors to activated by a row select (RS) signal to enable read/write operators
Basic cross-coupled 2-inverter latch with 2 stable op points for storing one-bit
SRAM cell is accessed via two bit (column) lines C and its complement for reliable operation
undoped polysilicon resistor
346

## Slide 45: 6T-SRAM
VDD
bit line C
bit line C
word line
word line
Full CMOS SRAM
Cell
VDD
bit line C
bit line C
word line
word line
Depletion-Load
SRAM Cell
347

## Slide 46: SRAM Operation Principles
VDD
bit line C
bit line C
R
R
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
RS=0: The word line is not selected. M3 and M4 are OFF
One data-bit is held: The latch preserves one of its two stable states.
If RS=0 for all rows: CC and CC are charged up to near VDD by pulling up of MP1 and MP2 (both in saturation)
Pull-up transistor (one per column)
348

## Slide 47: SRAM Operation Principles (Cont.)
RS=1: The word line is now selected. M3 and M4 are ON
Four Operations
Write “1” Operation (V1=VOL, V2=VOH at t=0-):
VC  VOL by the data-write circuitry. Therefore, V2  VOL, then M1 tur
off V1VOH and M2 turns on pulling down V2  VOL.
VDD
bit line C
bit line C
R
R
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
Pull-up transistor (one per column)
349

## Slide 48: SRAM Operation Principles (Cont.)
Read “1” Operation (V1=VOH, V2=VOL at t=0-):
VC retains pre-charge level, while VC  VOL by M2 ON. Data-read circuitry detects small voltage difference VC – VC > 0, and amplifies it as a “1” data output.
VDD
bit line C
bit line C
R
R
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
Pull-up transistor (one per column)
350

## Slide 49: SRAM Operation Principles (Cont.)
Write “0” Operation (V1=VOH, V2=VOL at t=0-):
VC  VOL by the data-write circuitry.
Since V1  VOL, M2 turns off, therefore V2  VOH.
VDD
bit line C
bit line C
R
R
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
Pull-up transistor (one per column)
351

## Slide 50: SRAM Operation Principles (Cont.)
Read “0” Operation (V1=VOL, V2=VOH at t=0-):
VC retains pre-charge level, while VC  VOL by M1 ON.
Data-read circuitry detects small voltage difference VC – VC < 0, and
amplifies it as a “0” data output.
VDD
bit line C
bit line C
R
R
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
Pull-up transistor (one per column)
352

## Slide 51: SRAM Operation Principles (Cont.)
3. Write “0” Operation (V1=VOH, V2=VOL at t=0-):
VC  VOL by the data-write circuitry.
Since V1  VOL, M2 turns off, therefore V2  VOH.
VDD
bit line C
bit line C
R
R
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
Pull-up transistor (one per column)
353

## Slide 52: SRAM Operation Principles (Cont.)
4. Read “0” Operation (V1=VOL, V2=VOH at t=0-):
VC retains pre-charge level, while VC  VOL by M1 ON.
Data-read circuitry detects small voltage difference VC – VC < 0,
and amplifies it as a “0” data output.
VDD
bit line C
bit line C
R
R
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
Pull-up transistor (one per column)
354

## Slide 53: Circuit of CMOS SRAM Cell
Advantages
  Very low standby power consumption
  Large noise margins than R-load SRAMS
  Operate at lower supply voltages than R-load SRAMS
Disadvantages
  Larger die area: To accommodate the n-well for pMOS transistors and polysilicon contacts. The area has been reduced by using multi- layer polysilicon and multi-layer metal processes
  CMOS more complex process
bit line C
bit line C
word line
VDD
VDD
CC
CC
M1
M2
M3
M4
MP1
MP2
V1
V2
VC
VC
RS
Pull-up transistor (one per column)
M5
355
M6
(Column voltages can reach to full VDD)
VDD

## Slide 54: Dynamic Read-Write Memory (DRAM) Circuits
M3
M4
SRAM: 4~6 transistors per bit
4~5 lines connecting as charge on capacitor
DRAM: Data bit is stored as charge on capacitor Reduced die area
Require periodic refresh
WL
BL
BL
M1
M2
parasitic storage
capacitances
Four-Transistor DRAM Cell
356

## Slide 55: DRAM Circuits (Cont.)
M3
WL(read)
BL(write)
M1
M2
parasitic storage
capacitances
WL(write)
BL(read)
Three-Transistor DRAM Cell
No constraints on device ratios Reads are non-destructive
Value stored at node X when writing a “1” = VWWL-VTn
357
X

## Slide 56: 3T-DRAM — Layout
BLR
358
BLW
GND
RWL
M3
M2
WWL
M1
Source: Digital Integrated Circuits 2nd

## Slide 57: One-Transistor DRAM Cell
M1
explicit storage
capacitances
WL
359
BL
One-Transistor DRAM Cell
Industry standard for high density dram arrays
Smallest component count and silicon area per bit
Separate or “explicit” capacitor (dual poly) per cell

## Slide 58: Operation of Three-Transistor DRAM Cell
The binary information is stored as the charge in C1
Storage transistor M2 is on or off depending on the charge in C1
Pass transistors M1 and M3: access switches
Two separate bit lines for “data read” and “data write”
M2
RS
DATA
M1
M3
MP1 MP2
VDD
C1
C2
Precharge devices
PC
C3
WS
Data_in Data_out
C2, C3 >> C1(>10C1)
360

## Slide 59: Operation of Three-Transistor DRAM Cell (Cont.)
The operation is based on a two-phase non-overlapping clock scheme
» The precharge events are driven by 1, and the “read” and “write”
operations are driven by 2.
» Every “read” and “write” operation is preceded by a precharge
cycle, which is initiated with PC going high.
M2
RS
DATA
M1
M3
WS
MP1
MP2
VDD
C1
C2
Precharge devices
PC
C3
Data_in
Data_out
PC
WS
DATA
PC write 1 PC
① 2 ③
read 1 PC write 0 PC read 0
4 ⑤ 6 ⑦ 8
Din
Stored data
RS
Dout
361

## Slide 60: Operation of Three-Transistor DRAM Cell (Cont.)
MP1 MP2
VDD
C2
Precharge devices
PC
Pre-charge Cycle
C3
RS
M2
DATA
Write “1” OP: DATA = 0, WS = 1; RS = 0
» C2, C1 Share charge due to M1 ON
» Since C2 >> C1, the storage node C1 attains approximately the same logic level.
M1
M3
WS
C1
C2
C3
Data_in
Data_out
362

## Slide 61: Operation of Three-Transistor DRAM Cell (Cont.)
RS
M2
DATA
Read “1” OP: DATA = 0, WS = 0; RS = 1
» M2, M3 ON  C3, C1 discharges through M2 and M3, and the falling column voltage is interpreted bt the “data read” circuitry as a stored logic “1”.
M1
M3
WS
C1
C2
C3
Data_in
Data_out
363

## Slide 62: Operation of Three-Transistor DRAM Cell (Cont.)
Write “0” OP: DATA = 1, WS = 1; RS = 0
» M2, M3 ON  C2 and C1 discharge to 0 through M1 and data_in nMOS.
RS
M2
DATA
M
1
M3
WS
C1
C
2
C
3
Data_in
Data_out
364

## Slide 63: Operation of Three-Transistor DRAM Cell (Cont.)
RS
M2
DATA
Read “0” OP: DATA = 1, WS = 0; RS = 1
» C3 does not discharge due to M2 OFF, and the logic-high level on the Data_out column is interpreted by the data read circuitry as a stored “0” bit.
M1
M3
WS
C1
C2
C3
Data_in
Data_out
365

## Slide 64: Operation of One-Transistor DRAM Cell
Write “1” OP: BL = 1, WL = 1 (M1 ON)C1 charges to “1”
Write “0” OP: BL = 0, WL = 1 (M1 ON)C1 discharges to “0”
Read OP: destroys stored charge on C1  destructive refresh is
needed after every data read operation
BL
M1
WL
C
1
C
366
2
Column
capacitance
1-bit DRAM Cell
C2>>C1

## Slide 65: SRAM
RAM
DRAM
WL
DL
VDD
WL
367
WL
DL
DL

## Slide 66: Semiconductor Memory Types (Cont.)
368
ROM: 1, nonvolatile memories
2, only can access data, cannot to modify data
3, lower cost: used for permanent memory in printers, fax, and game machines, and ID cards
  Mask ROM: data are written during chip fabrication by a photo mask
  PROM: data are written electrically after the chip is fabricated.
» Fuse ROM: data cannot be erased and modified.
» EPROM and EEPROM: data can be rewritten, but the number of subsequent re-write operations is limited to 104-105.
    EPROM uses ultraviolet rays which can penetrate through the crystal glass on package to erase whole data simultaneously.
    EEPROM uses high electrical voltage to erase data in 8 bit units.
  Flash Memory: similar to EEPROM

## Slide 67: ROM: “Read-Only” Memory
Nonvolatile
Can be read from but not written to, by a
processor in an microcomputer system
Traditionally written to, “programmed”,
before inserting to microcomputer system
Uses
Store software program for general-purpose processor
Store constant data (parameters) needed by system
Implement combinational circuits (e.g., decoders)
2k × n ROM
Q0
…
Qn-1
A0
…
enable
369
Ak-1
External view

## Slide 68: Example: 8 x 4 ROM
Horizontal lines = words
Vertical lines = data
Lines connected only at circles
Decoder sets word 2’s line to 1 if
address input is 010
Data lines Q3 and Q1 are set to 1 because there is a “programmed” connection with word 2’s line
Word 2 is not connected with data
lines Q2 and Q0
Output is 1010
8 × 4 ROM
3×8
decoder
enabl
Ae
0
A1
A2
Q3 Q2 Q1 Q0
programm
able
connection
data line
word 0
word 1
word 2
word
line
370
Internal view

## Slide 69
371
Memory – ROM
Nonvolatile Memory
  SRAM and DRAM and attractive due to their speed
  however, they are volatile which means when the power is removed, the data is lost
  for a microcomputer, we need a nonvolatile storage device so that upon power-up, the computer knows what to do.
  currently, the most popular semiconductor ROM is Flash (or EEprom)
  before looking at the details of a Flash transistor, let’s first look at the
different types of ROM arrays and addressing modes

## Slide 70: Memory – ROM
ROM Arrays
  There are two basic types of ROM arrays
    NOR-based ROM
    NAND-based ROM
NOR-based ROM
  All Column Lines are pulled-up using a PMOS transistor (or resistor)
  The Row Lines are connected to the gates of NMOS transistors at the intersection of Row and Column Lines
  The presence or absence of the NMOS transistors dictates whether a 1 or a 0 is stored
  If the NMOS transistor is present, it will pull down the Column Line when its gate is driven high by the Row Line
  If the NMOS transistor is absent, the Column Line will not be pulled down, so it will
37r2emain pulled up by the PMOS’s

## Slide 71: Memory – ROM
NOR-based ROM
In order to Read from the array, the Row line is asserted and the desired Column line is observed
a NOR-based ROM is similar to a Hex Keypad
373

## Slide 72: Memory – ROM
NAND-based ROM
  NAND-based ROM is a different array architecture
  it uses a depletion-load NMOS as the pull-up transistor
  the Column NMOS’s are connected in series with the
column lines (i.e. a NAND configuration)
  If an NMOS exists in the Column line and the Row line is asserted, the NMOS will pull the Column Line down and represent a stored ’0’
  If an NMOS is absent on the Column line and the Row line is asserted, the Column Line will remain pulled high by the depletion NMOS and represent a stored ‘1’
  since all of the NMOS’s are in series, in order to Read
from a Row, all other Rows much be turned ON
  this means in order to distinguish the Row we are asserting,
we write a ‘0’ to it
374

## Slide 73: Memory – ROM
NAND-based ROM
  In this configuration, if an NMOS is present, it will represent a “stored 1” since in order to address its location, the Row line is driven to a ‘0’ and the NMOS not turned on. This leaves the Column line pulled HIGH
  if an NMOS is absent, it will represent a “stored 0” since all of the other Row NMOS’s are turned on and will pull the Column Line LOW
  this gives the opposite behavior as in a NOR-based ROM
 | NOR | NAND
NMOS present | 0 | 1
NMOS absent | 1 | 0
- it also gives a complementary addressing scheme
 | NOR | NAND
Address Row Line by driving: | 1 | 0
All other Row Lines driven to: | 0 | 1
375

## Slide 74: Mask-programmed ROM
Connections “programmed” at fabrication
  set of masks
Lowest write ability
  only once
Highest storage permanence
  bits never change unless damaged
Typically used for final design of high-volume systems
  spread out NRE (non-recurrent engineering) cost for a low unit cost
376

## Slide 75: OTP ROM: One-time programmable ROM
377
Connections “programmed” after manufacture by user
  user provides file of desired contents of ROM
  file input to machine called ROM programmer
  each programmable connection is a fuse
  ROM programmer blows fuses where connections should not exist
Very low write ability
  typically written only once and requires ROM programmer device
Very high storage permanence
  bits don’t change unless reconnected to programmer and more fuses
blown
Commonly used in final products
  cheaper, harder to inadvertently modify

## Slide 76: EPROM: Erasable programmable ROM
.
(d)
(a)
(b)
source
drain
+15V
source
drain
0V
(c)
source
drain
floating gate
5-30 min
Programmable component is a MOS transistor
Transistor has “floating” gate surrounded by an insulator
(a) Negative charges form a channel between source and drain storing a logic 1
(b) Large positive voltage at gate causes negative charges to move out of channel and get trapped in floating gate storing a logic 0
(c) (Erase) Shining UV rays on surface of floating-gate causes negative charges to return to channel from floating gate restoring the logic 1
(d) An EPROM package showing quartz window through which UV light can pass
Better write ability
  can be erased and reprogrammed thousands of times
Reduced storage permanence
  program lasts about 10 years but is susceptible to radiation and electric noise
Typically used during design development
378

## Slide 77: Sample EPROM components
379

## Slide 78: Sample EPROM programmers
380

## Slide 79: EEPROM: Electrically erasable programmable ROM
381
Programmed and erased electronically
  typically by using higher than normal voltage
  can program and erase individual words
Better write ability
  can be in-system programmable with built-in circuit to provide higher
than normal voltage
» built-in memory controller commonly used to hide details from memory user
  writes very slow due to erasing and programming
» “busy” pin indicates to processor EEPROM still writing
  can be erased and programmed tens of thousands of times
Similar storage permanence to EPROM (about 10 years)
Far more convenient than EPROMs, but more expensive

## Slide 80: FLASH
382
Extension of EEPROM
  Same floating gate principle
  Same write ability and storage permanence
Fast erase
  Large blocks of memory erased at once, rather than one word at a time
  Blocks typically several thousand bytes large
Writes to single words may be slower
  Entire block must be read, word updated, then entire block written back
Used with embedded microcomputer systems storing large data
items in nonvolatile memory
  e.g., digital cameras, MP3, cell phones

## Slide 81: Serial Access Memories
383
Serial access memories do not use an address
– Shift Registers
– Serial In Parallel Out (SIPO)
– Parallel In Serial Out (PISO)
– Queues (FIFO, LIFO)

## Slide 82
384

## Slide 83
385

## Slide 84
386

## Slide 85: SEMICONDUCTOR INTEGRATED CIRCUIT
DESIGN
Programmable Logic Array (PLA)
Programmable
Array Logic(PAL)
FPGAs
CPLDs
Standard cells
Design Approach
Parameters influencing low power design
Programmable logic devices (PLD)
400

## Slide 86: Programmable logic is defined as a device with configurable
402
PLD
with programmable
logic and flip-flops linked together interconnect.
Why we are going for PLDs
Problems by Using Basic Gates
Many components on PCB:
As no. of components rise, nodes interconnection complexity grow exponentially
Growth in interconnection will cause increase in interference, PCB size, PCB
design cost, and manufacturing time

## Slide 87: PROGRAMMABLE LOGIC DEVICES (PLD)
PLD Hierarchical Architecture
405

## Slide 88
406
PLD
The purpose of a PLD device is to permit elaborate digital logic designs to be implemented by the user in a single device.
Can be erased electrically and reprogrammed with a new design, making them very well suited for academic and prototyping
Types of Programmable Logic Devices
SPLDs (Simple Programmable Logic Devices)
  ROM (Read-Only Memory)
  PLA (Programmable Logic Array)
  PAL (Programmable Array Logic)
  GAL (Generic Array Logic)
CPLD (Complex Programmable Logic Device)
FPGA (Field-Programmable Gate Array)

## Slide 89: General structure of PLDs.
407

## Slide 90
408
PLD
The first three varieties(ROM, PLA, PAL) are quite similar to each other:
  They all have an input connection matrix, which connects the inputs of the device to an array of AND- gates.
  They all have an output connection matrix, which connect the outputs of the AND-gates to the inputs of OR-gates which drive the outputs of the device.
The gate array is significantly different and will be described later.

## Slide 91
PLD
The differences between the first three categories are these:
  1. In a ROM, the input connection matrix is hardwired.
The user can modify the output connection matrix.
  In a PAL/GAL the output connection matrix is hardwired. The user can modify the input connection matrix.
  In a PLA the user can modify both the input connection matrix and the output connection matrix.
409

## Slide 92: Programming by blowing fuses.
(a) Before programming.
(b) After programming.
410

## Slide 93: OR - PLD Notation
411

## Slide 94: AND - PLD Notation
412

## Slide 95
413

## Slide 96
PLA
414

## Slide 97
PLA
415
A 3×2 PLA with 4 product terms.

## Slide 98: JK FF implementation using PLA
416

## Slide 99: PALs
42
5
Programmable Array Logic
  a fixed OR array.
 | Inputs Dense array of AND gates |  | Product terms | Dense array of OR gates |  | 
 |  |  |  |  | Outputs | 

## Slide 100: A simple four-input, three-output PAL device.
426

## Slide 101: An example of using a PAL device to realize two Boolean functions. (a) Karnaugh maps. (b) Realization.
427

## Slide 102: PAL
x x
428
x
W = ABC + CD
X = ABC + ACD + ACD + BCD
Y = ACD + ACD + ABD

## Slide 103: FPGA AND CPLD
429
FPGA - Field-Programmable Gate Array.
CPLD - Complex Programmable Logic Device
FPGA and CPLD is an advance PLD.
Support thousands of gate where as PLD only support hundreds of gates.

## Slide 104: What is an FPGA?
430
Before the advent of programmable logic, custom logic circuits were built at the board level using standard components, or at the gate level in expensive application-specific (custom) integrated circuits.
FPGA is an integrated circuit that contains many (64 to over 10,000) identical logic cells that can be viewed as standard components. Each logic cell can independently take on any one of a limited set of personalities.
Individual cells are interconnected by a matrix of wires and programmable switches. A user's design is implemented by specifying the simple logic function for each cell and selectively closing the switches in the interconnect matrix.
Array of logic cells and interconnect form a fabric of basic building blocks for logic circuits. Complex designs are created by combining these basic blocks to create the desired circuit

## Slide 105: What does a logic cell do?
431
The logic cell architecture varies between different device families.
Each logic cell combines a few binary inputs (typically between 3 and
10) to one or two outputs according to a Boolean logic function
specified in the user program .
In most families, the user also has the option of registering the combinatorial output of the cell, so that clocked logic can be easily implemented.
Cell's combinatorial logic may be physically implemented as a small look-up table memory (LUT) or as a set of multiplexers and gates.
LUT devices tend to be a bit more flexible and provide more inputs
per cell than multiplexer cells at the expense of propagation delay.

## Slide 106: What does 'Field Programmable' mean?
432
Field Programmable means that the FPGA's function is defined by a user's program rather than by the manufacturer of the device.
A typical integrated circuit performs a particular function defined at the time of manufacture. In contrast, the FPGA's function is defined by a program written by someone other than the device manufacturer.
Depending on the particular device, the program is either 'burned' in permanently or semi-permanently as part of a board assembly process, or is loaded from an external memory each time the device is powered up.
This user programmability gives the user access to complex integrated designs without the high engineering costs associated with application specific integrated circuits.

## Slide 107: How are FPGA programs created?
433
Individually defining the many switch connections and cell logic functions would be a daunting task.
This task is handled by special software. The software translates a user's schematic diagrams or textual hardware description language code then places and routes the translated design.
Most of the software packages have hooks to allow the user to influence implementation, placement and routing to obtain better performance and utilization of the device.
Libraries of more complex function macros (eg. adders) further simplify the design process by providing common circuits that are already optimized for speed or area.

## Slide 108: FPGA
434
FPGA applications:-
  DSP
  Software-defined radio
  Aerospace
  Defense system
  ASIC Prototyping
  Medical Imaging
  Computer vision
  Speech Recognition
  Cryptography
  Bioinformatic
  And others.

## Slide 109
436
FPGA Principles
A Field-Programmable Gate Array (FPGA) is an integrated circuit that can be configured by the user to emulate any digital circuit as long as there are enough resources
An FPGA can be seen as an array of Configurable Logic Blocks (CLBs) connected through programmable interconnect (Switch Boxes)

## Slide 110: FPGA structure
CLB
SB
SB
SB
CLB
SB
SB
CLB
CLB |  |  |  | 
Configurable Logic Blocks
Interconnection Network
I/O Signals (Pins)
437

## Slide 111: Simplified CLB Structure
CLB
SB
SB
SB
CLB
SB
SB
CLB
CLB |  |  |  | 
Configurable Logic Blocks
Interconnection Network
I/O Signals (Pins)
Look-Up Table (LUT)
Q
SET
CLR Q
D
MUX

## Slide 112: Example: 4-input AND gate
A B
C D
O
A | B | C | D | O
0 | 0 | 0 | 0 | 0
0 | 0 | 0 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0
0 | 1 | 0 | 0 | 0
0 | 1 | 0 | 1 | 0
0 | 1 | 1 | 0 | 0
0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 0 | 0
1 | 0 | 0 | 1 | 0
1 | 0 | 1 | 0 | 0
1 | 0 | 1 | 1 | 0
1 | 1 | 0 | 0 | 0
1 | 1 | 0 | 1 | 0
1 | 1 | 1 | 0 | 0
1 | 1 | 1 | 1 | 1
Q
SET
CLR Q
D
MUX
A B
C D
0
0
0
0
0
0
0
0
0
0
0
0
0
0
0
1
Configuration bits
O
0
6/3/2015

## Slide 113: Example 2: Find the configuration bits for the following circuit
Q
SET
CLR Q
D
2-to-1
MUX
A0
A1
S
Clock
SET
CLR Q
D Q
MUX
A0 A1
S
Configuration bits
A0 | A1 | S | 
0 | 0 | 0 | 
0 | 0 | 1 | 
0 | 1 | 0 | 
0 | 1 | 1 | 
1 | 0 | 0 | 
1 | 0 | 1 | 
1 | 1 | 0 | 
/3/ 1 | 1 | 1 | 
6

## Slide 114: Interconnection Network
CLB
SB
SB
SB
CLB
SB
CLB
SB
CLB
Configurable Logic Blocks
Interconnection Network
I/O Signals (Pins)
Configuration
bits
1
0
0
0
0
0

## Slide 115: Example 3
Determine the configuration bits for the following circuit implementation in a 2x2 FPGA, with I/O constraints as shown in the following figure. Assume 2-input LUTs in each CLB.
CLB0
SB0
SB1
SB2
CLB1
SB3
SB4
CLB3
CLB2 |  |  |  | 
Input1
Input2
Output
Input3
SET
CLR Q
D Q
Input1 Input2
Input3
Output

## Slide 116: CLBs required
SET
CLR Q
D Q
Input1 Input2
Input3
Output
CLB 1
CLB 2
SET
CLR Q
D Q
MUX
Input1 Input2
0
0
0
1
Configuration bits
O
1
SET
CLR Q
D Q
MUX
O
Input3
0
1
1
0
Configuration bits
Output
0

## Slide 117: Placement: Select CLBs
CLB0
SB0
SB1
SB2
CLB1
SB3
SB4
CLB3
CLB2 |  |  |  | 
Input1
444
Input2
Output
Input3

## Slide 118: Routing: Select path
CLB0 |  |  |  | SB0 |  |  |  |  | CLB1 |  |  | 
SB1 |  |  |  | SB2 |  |  |  |  | SB3 |  |  | 
CLB2 |  |  |  | SB4 |  |  |  |  | CLB3 |  |  | 
Input1
Input2
Output
Input3
Configuration bits
SB1
0
0
0
0
1
0
Configuration bits
SB4
0
0
1
0
445

## Slide 119: Configuration Bitstream
446
The configuration bitstream must include ALL CLBs and SBs, even unused ones
CLB0: 00011
CLB1: 01100
CLB2: XXXXX
CLB3: ?????
SB0: 000000
SB1: 000010
SB2: 000000
SB3: 000000
SB4: 000001

## Slide 120: FPGA Advantages
447
Long time availability
Can be updated and upgraded at your customer's site
Extremely short time to market
Fast and efficient systems
Performance gain for software applications
Real time applications
Massively parallel data processing

## Slide 121
FPGA EDA Tools
 Must provide a design environment based on digital design concepts and components (gates, flip-flops, MUXs, etc.)
 Must hide the complexities of placement, routing and bitstream generation from the user. Manual placement, routing and bitstream generation is infeasible for practical FPGA array sizes and circuit complexities.
448

## Slide 122: Design of approach of IC
449

## Slide 123
450

## Slide 124
451
Silicon Wafers: Basic unit
Silicon Wafers Basic processing unit
150, 200, 300 mm disk, 0.5 mm thick
Newest ones 300 mm (12 inches)
Typical process 25 - 1000 wafers/run
Each wafer: 100 - 1000's of microchips (die)
Wafer cost $10 - $100's
200 mm wafer weight 0.040 Kg
Typical processing costs $1200/wafer (200
mm)
Typical processed wafer value $11,000
(all products, modest yield)
Value/Mass of processed wafer $275,000/Kg

## Slide 125: CPLD
452
1.
2.
Complexity of CPLD is between FPGA and PLD.
CPLD featured in common PLD:-
i. Non-volatile configuration memory – does not need an external configuration PROM.
ii. Routing constraints. Not for large and deeply layered logic.
3.
CPLD featured in common FPGA:-
i. Large number of gates available.
ii. Can include complicated feedback path.
4.
CPLD application:-
i. Address coding
High performance control logic
Complex finite state machines

## Slide 126: CPLD
5. CPLD architecture:-
LAB – Logic Array Block / uses PALs
PIA – Programmable Interconnect Array
453

## Slide 127: PROM Notation
454